## Slide 1
Switching OFF procedure for the Olympus FV1000
Follow the order!
If Argon laser was on
AND it will not be used within 2 hours:
1. Key
Wait till fan of the Argon laser has cooled down +/- 15 min
After the 15 minutes of argon laser off:
7. Button
5. Exit software
6. Shut down PC
In the meantime you can switch off:
2. (if on And if next user will not use it ) Fluorescence lamp
9. Main buttons (from right to left, starting with fluorescence)
If 559 laser was on:
3. Key
4. Button
5. Exit software
6. Close PC
1
2
4
3
7
9
8. Laser controler
8
10. Close microscope shutter (you get warning….
10
Note: As key is broken use the screwdriver
Only do this!!
Notes: Add note about warning microscope shutter